## Slide 1: Burst-MAC: A MAC Protocol for Handling Burst Traffic in LoRa Network
Aakriti Jain1, Md Ashikul Haque1, Abusayeed Saifullah1, Haibo Zhang2
1 Wayne State University, USA
2 University of Otago, New Zealand
IEEE RTSS 2024, York, United Kingdom

## Slide 2
Low Power Wide Area Network (LPWAN) has enabled various IoT applications.
Low Power Wide Area Network
Agriculture Monitoring
Smart City
Smart Metering
Wide coverage
High capacity
Long battery life
Low Cost
(Long Range)
Environment Monitoring
5.9 million gateways and 300 million end nodes with LoRa deployed worldwide,
over 600 documented use cases (May 2024).
https://www.semtech.com/lora
Credits to LoRa Alliance
Notes: The growing demand for Internet-of-Things (IoT) applications has led to the development of several Low-Power Wide-Area Network (LPWAN) technologies in recent years.
Lora Operates in unlicensed sub-GHz band, and facilitates
long-range connectivity ,
low power consumption,
and low data-rate transmissions
It's widely available worldwide, with over 600 documented use cases such as

## Slide 3
End Devices (nodes), Gateway, Network Server.
Communication Path/ Channel:
    Nodes transmit packets to gateway via Uplink channel.
    Gateway communicates with nodes via Downlink channel.
Chirp Spread Spectrum (CSS) technology.
Spreading Factor (SF): implies the no. of raw bits encoded in a symbol. (SF 7-12)
LoRa Overview
Fig: LoRa network architecture
Notes: A typical LoRa architecture includes many end-devices or (LoRa nodes), one or more gateways and a network server. Nodes are sensors/actuators that directly communicate with the gateway wirelessly over long-range.
LoRa is the PHY layer of LoRa stack while LoRaWAN is the MAC layer.
LoRaWAN divides the available
spectrum into multiple uplink and downlink channels. Nodes
send data to the gateway on the uplink channels and the
gateway responds on the downlink channels.
LoRa uses CSS modulation technique and offers several runtime-adjustable transmission parameters, out of which spreading factor is a major one.

## Slide 4
Fig: Forest fire monitoring in California forest
state foresters California
Credits:
LoRa is typically designed to handle very infrequent communications.
LoRa Overview

## Slide 5
What is Burst Traffic?
Numerous nodes start transmitting data packets simultaneously in quick succession.
Leads to temporary surge in network activity ⚠️
Fig: California Wildfire (2021)
Credits: The Nature Conservancy
However, many applications experience Burst Traffic. E.g., emergencies like Forrest Fire, Volcanic Eruption, Earthquake, or Smart Cities during peak hours.
Notes: However, upon detecting a fire
sensors near the affected area begin generating burst traffic,
likely indicating intense heat or smoke.
All nodes start transmitting data packets to the gateway simultaneously in a quick succession leading to temp surge in network traffic.
This sudden uptick in data transmission plays a pivotal role in
alerting authorities and facilitating timely responses such as
evacuation in the event of a fire or eruption.

## Slide 6
Consequences of Burst Traffic in LoRa
914.2
915
915.8
Frequency (MHz)

## Slide 7
914.2
915
915.8
Frequency (MHz)
Collisions
Consequences of Burst Traffic in LoRa

## Slide 8
914.2
915
915.8
Frequency (MHz)
Collisions
*Validation from experiment in our lab
Current MAC protocol of LoRa: LoRaWAN adopts ALOHA NO collision avoidance mechanism!
Increased packet loss*
Increased retransmissions
Rapid battery depletion
Excessive network latencies
Degraded throughput*
Why is it necessary to handle Burst Traffic?
Fig: Packet Reception Rate for 5 nodes
Single channel
Notes: LoRaWAN-
34.54
26.81
20.77
13.35
9.39

## Slide 9
914.2
915
915.8
Frequency (MHz)
Collisions
*Validation from experiment in our lab
Current MAC protocol of LoRa: LoRaWAN adopts ALOHA NO collision avoidance mechanism!
Increased packet loss*
Increased retransmissions
Rapid battery depletion
Excessive network latencies
Degraded throughput*
Why is it necessary to handle Burst Traffic?
Fig: Packet Reception Rate for 5 nodes
Ensuring successful transmission of this traffic without loss is critical
Notes: Ensuring successful transmission of this traffic without loss is critical to alert authorities and enable timely responses.

## Slide 10
Semi-Distributed Scheduling Mechanism.
    Nodes compute their Tx slots individually.
    Eliminates the need of centralized slot distribution.
Devices switch to Burst-MAC only when burst is detected.
    Work in LoRaWAN mode otherwise.
    No time synchronization required during non-burst periods!
Burst-MAC
We introduce Burst-MAC, a low-overhead and bounded latency MAC protocol for LoRa networks to handle burst traffic.
Fig: Nodes in the effected area undergo burst and switch to Burst-MAC. Nodes in non-effected areas work in LoRaWAN mode.

## Slide 11
Exploits parallel packet reception capability of LoRa gateway by using Orthogonal Virtual Channels (VC).
Burst-MAC
frequency
125
250
500 kHz
Bandwidth
(BW)
Spreading Factor (SF)
time
frequency
SF7
SF8
SF9
…
<Physical Channel (Central Frequency, Bandwidth), Spreading Factor> Virtual channel
e.g., <Ch 1, SF 7> -> VC 1
<Ch 1, SF 8> -> VC 2
<Ch 4, SF 9> -> VC 3

## Slide 12
Burst-MAC Design
Determining the Start of Burst Traffic
packet generation exceeded threshold?
Burst!
+ Collisions exceeded threshold?
Burst Detected!
Explicit Feedback- Nodes under burst
uplink
Switch to Burst-MAC
Piggybacked ACK
Notes: Gateway-
Identifies burst when VC collisions exceed a predefined threshold.
to burst nodes.
    Beacons provide a timing reference for clock synchronization with gateway.
Thereafter, they use Burst-MAC for subsequent transmissions. Note that, it is not required for the gateway and the burst nodes to switch to Burst-MAC at the same time. A burst node can switch to Burst-MAC once it detects burst or receives the notification from the gateway

## Slide 13
Gateway groups the nodes based on their VC.
    Only a few nodes per group.
Each VC is a unique group.
    Collisions confined within groups.
    Enables concurrent transmissions.
    Now collisions need to resolved only inside each VC, which can be done using a transmission scheduling policy.
Burst-MAC Design
Grouping Nodes based on Virtual Channels
LoRa in the US, mup uplink channels and s total number of SF
902
904
928
Frequency (MHz)
903
927
s= 6, mup = 64
Virtual Channels: 6 64 = 384
Hundreds of Virtual Uplink Channels.

## Slide 14
Nodes in burst mode within a VC individually compute their time slots for uplink transmission using a hash function, e.g.,
Burst-MAC Design
Hash-based Scheduling for Uplink Transmissions
h(K) = k mod M
Hash value
Node ID
No. of nodes in a group
Hash value = node’s uplink Tx time slot,
n0
n6
n1
n5
n2
n4
n3
n9
n8
n7
ID 1230 1231 1232 1243 1244 1235 1245 1266 1287 1299
Superframe defines the total no. of time slots for a group
Hash-based semi-distributed transmission scheduling policy!
Notes: Naturally synchronized

## Slide 15
Burst-MAC Design
Hash-based Scheduling for Uplink Transmissions
n0
n6
n1
n5
n2
n4
n3
n9
n8
n7
ID 1230 1231 1232 1243 1244 1235 1245 1266 1287 1299
h(K) = k mod M
Time Slot = Node ID % 10
Time
slots
0
Superframe length = 10
1
2
3
4
5
6
7
5
9

## Slide 16
Burst-MAC Design
Ensuring Collision Free Transmissions
n0
n6
n1
n5
n2
n4
n3
n9
n8
n7
ID 1230 1231 1232 1243 1244 1235 1245 1266 1287 1299
Time
slots
0 1 2 3 4 5 5 6 7 9
Collision!!
Burst-MAC dynamically handles time slot collisions.
New time slot via Piggybacked ACK

## Slide 17
Burst-MAC Design
Ensuring Collision Free Transmissions
n0
n6
n1
n5
n2
n4
n3
n9
n8
n7
ID 1230 1231 1232 1243 1244 1235 1245 1266 1287 1299
Time
slots
0 1 2 3 4 5 8 6 7 9
Collision Resolved!!
Burst-MAC maximizes overall utilization.
Ensures Bounded Latencies for every packet.
Before collision resolution: 2 * Ni time slots
After collision resolution: Ni time slots
Where, Ni = superframe length
Notes: Bounded Latencies for successful uplink packets only. We do not consider lost packets

## Slide 18
Burst-MAC Design
Downlink Communication in Burst-MAC
To ensure new schedules are received successfully, burst nodes work in Class-B mode.
    Nodes can receive ACKs in either RX1, RX2, or additional ping slots. More chances to receive downlink ACK containing new Tx slots.
Fig: Class-B mode of LoRa
Increases chances of successful collision resolution

## Slide 19
Burst-MAC Design
Final Collision Free Transmission Slots look like
n0
n6
n1
n5
n2
n4
n3
n9
n8
n7
ID 1230 1231 1232 1243 1244 1235 1245 1266 1287 1299
Time
slots
0 1 2 3 4 5 8 6 7 9
t0 | t1 | t2 | t3 | t4 | t5 | t6 | t7 | t8 | t9 | t0 | t1 | t2 | t3 | t4 | t5 | t6 | t7 | t8 | t9
n0 n1 n2 n3 n4 n5 n7 n8 n6 n9
n0 n1 n2 n3 n4 n5 n7 n8 n6 n9
Pkt1
Pkt 2/ ReTx
Round 1 Tx
Round 2 Tx
One Superframe (within one VC)

## Slide 20
Burst-MAC Design
Handling the end of Burst Traffic
packet generation within threshold?
Burst End!
+ Increased no. of unused slots?
Burst End!
Explicit Feedback- Nodes ended
uplink
Transition from Class-B to Class-A. Stop computing tx slots.
End Burst-MAC. Stop sending any schedules.

## Slide 21
Aakriti Jain
aakriti.jain@utdallas.edu
Read my paper at:
DOI: 10.1109/RTSS62706.2024.00022
Thank you!